## Slide 1
Common Clock Framework (CCF)
- Khushal

## Slide 2
Agenda
Introduction
Overview of clock tree
Main Contents include
Overview of CCF
Implementation of CCF core
Hardware Clock Operations

## Slide 3
Introduction
Clock framework use to manage the clock resources of the system.
Its divided in three parts:
        Provide generic API to other drivers for operating clocks.
        General logic for provide clock control, will be independent of hardware.
        The hardware related clock control logic is encapsulated into operation function (ops).
Hardware specific code will be access by framework using ops.

## Slide 4
Overview of clock tree
TCXO
GPLL0
GPLL1
GPLL-n
RCG
CBC0
CBC1
CBC-n
HW0
HW1
HW2
0
1
2
3
4
5
6
7

## Slide 5
Overview of clock tree
Clock related devices include:
  TCXO = Crystal Oscillator,
  PLL = For phase multiplication (phase-locked loop)
  RCG = Divider for frequency division,
  Mux for multiplexing
  CBC = AND gate for clock enable control
  HW = Hardware module (consumers) using clock

## Slide 6
Main contents include
Enable/disable clk.
Set the frequency of clk.
Select the parent of clk.

## Slide 7
Clock driver common
Clock driver rcg2
Clock driver branch
Clock driver PLL
Clock driver OSM
Clock driver AOP
Clock driver RPMH
Device Driver
Device Tree
Uses the public clock APIs
clk_get/clk_put
clk_prepare/clk_unprepared
clk_set_rate
clk_enable/clk_disable
Describes:
Clocks and their relationships
Which clocks are needed for
the different devices
Uses the clk_ops operations
Uses the clk_ops operations
Provided by base clock framework
Provided by
driver code
Common clock framework
Clock driver fixed factor
Clock driver fixed rate
Clock driver divider
Clock driver mux
Overview of CCF

## Slide 8
Main contents include
Interface divided into two halves:
Common Clock Framework core
    Common definition of struct clk
    Common implementation of the clk.h API (defined in drivers/clk/clk.c)
    struct clk_ops: operations invoked by the clk API implementation. Not supposed to be modified when adding a new driver
Hardware-specific
    Callbacks registered with struct clk_ops and the corresponding hardware-specific structures
    Has to be written for each new hardware clock (struct clk_foo)
The two halves are tied together by struct clk_hw, which is defined in struct clk_foo and pointed to within struct clk.

## Slide 9
struct clk_core {
const char *name;
const struct clk_ops *ops;
struct clk_hw *hw;
struct module *owner;
struct clk_core *parent;
const char **parent_names;
struct clk_core **parents;
unsigned int num_parents;
unsigned int new_parent_index;
unsigned long rate;
unsigned long req_rate;
unsigned long new_rate;
struct clk_core *new_parent;
struct clk_core *new_child;
unsigned long flags;
bool orphan;
unsigned int enable_count;
unsigned int prepare_count;
bool need_handoff_enable;
bool need_handoff_prepare;
unsigned long min_rate;
unsigned long max_rate;
unsigned long accuracy;
int phase;
struct hlist_head children;
struct hlist_node child_node;
struct hlist_head clks;
unsigned int notifier_count;
#ifdef CONFIG_DEBUG_FS
struct dentry *dentry;
struct hlist_node debug_node;
#endif
struct kref ref;
struct clk_vdd_class *vdd_class;
unsigned long *rate_max;
int num_rate_max;
};
struct clk {
struct clk_core *core;
const char *dev_id;
const char *con_id;
unsigned long min_rate;
unsigned long max_rate;
struct hlist_node clks_node;
};
struct clk_hw {
struct clk_core *core;
struct clk *clk;
const struct clk_init_data *init;
};
struct clk_init_data {
const char *name;
const struct clk_ops *ops;
const char * const *parent_names;
unsigned int num_parents;
unsigned long flags;
struct clk_vdd_class *vdd_class;
unsigned long *rate_max;
int num_rate_max;
};
struct clk_vdd_class {
const char *class_name;
struct regulator **regulator;
int num_regulators;
int (*set_vdd)(struct clk_vdd_class *v_class, int level);
int *vdd_uv;
int *level_votes;
int num_levels;
bool skip_handoff;
bool use_max_uV;
unsigned long cur_level;
struct mutex lock;
};
/*
* flags used across common struct clk. these flags should only affect the
* top-level framework. custom flags for dealing with hardware specifics
* belong in struct clk_foo
*/
#define CLK_SET_RATE_GATE BIT(0) /* must be gated across rate change */
#define CLK_SET_PARENT_GATE BIT(1) /* must be gated across re-parent */
#define CLK_SET_RATE_PARENT BIT(2) /* propagate rate change up one level */
#define CLK_IGNORE_UNUSED BIT(3) /* do not gate even if unused */
/* unused */
#define CLK_IS_BASIC BIT(5) /* Basic clk, can't do a to_clk_foo() */
#define CLK_GET_RATE_NOCACHE BIT(6) /* do not use the cached clk rate */
#define CLK_SET_RATE_NO_REPARENT BIT(7) /* don't re-parent on rate change */
#define CLK_GET_ACCURACY_NOCACHE BIT(8) /* do not use the cached clk accuracy */
#define CLK_RECALC_NEW_RATES BIT(9) /* recalc rates after notifications */
#define CLK_SET_RATE_UNGATE BIT(10) /* clock needs to run to set rate */
#define CLK_IS_CRITICAL BIT(11) /* do not gate, ever */
/* parents need enable during gate/ungate, set rate and re-parent */
#define CLK_OPS_PARENT_ENABLE BIT(12)
#define CLK_ENABLE_HAND_OFF BIT(13) /* enable clock when registered. */
/*
* hand-off enable_count & prepare_count
* to first consumer that enables clk
*/
#define CLK_IS_MEASURE BIT(14) /* measure clock */
All implementation of the clock APIs are present in drivers/clk/clk.c
Implementation of CCF core

## Slide 10
Implementation defined in drivers/clk/clk.c.
Takes care of:
  Maintaining the clock tree
  Concurrency prevention (using a global spinlock for clk_enable()/clk_disable() and a global mutex for all other operations).
  Propagating the operations through the clock tree
  Notification when rate change occurs on a given clock, the register callback is called.
  Voltage vote : Voltage voting for the corresponding frequency of a given clock (QCOM Implementation)
  Debugfs extend & implement the below debugfs entries
    /sys/kernel/debug/clk |_ <clk_name> |_ clk_enable_count [R/W] |_ clk_rate [R/W] |_ clk_list_rates [QCOM R/W] |_ clk_rate_max [QCOM R/W] |_ clk_parent [No change] |_ clk_print_regs [QCOM R] |_ clk_measure [QCOM R] |_ debug_suspend [QCOM R/W] |_ clk_enabled_list [QCOM R]

## Slide 11
Hardware clock operations
The API is split in two pairs:
  .prepare(/.unprepare):
    Called to prepare the clock before actually ungating it.
    May sleep
    Must not be called in atomic context
  .enable(/.disable):
    Called to ungate the clock once it has been prepared
    Must not sleep
    Can be called in atomic context

## Slide 12
Hardware clock operations
.is_enabled: Instead of checking the enable count, querying the hardware to determine if the clock is enabled.
.round_rate:
  Returns the closest rate actually supported by the clock.
  Called by clk_round_rate() or by clk_set_rate() during propagation.
.set_rate:
  Changes the rate of the clock.
  Called by clk_set_rate() or during propagation.

## Slide 13
Hardware clock operations
.get_parent:
  Queries the hardware to determine the parent of a clock.
.set_parent:
  Changes the input source of this clock.
  Receives a index on in either the .parent_names or .parents arrays

## Slide 14
References
https://www.kernel.org/doc/Documentation/clk.txt

## Slide 15
Thanks