## Slide 1
Clock Tree
- Khushal

## Slide 2
Key words
CBC – Clock Branch Controller
GCC – Global Clock Controller
RCG – Root Clock Generator
PLL – Phase Locked Loop
GDSC – GloballyDistributed Switch Controller
CXO/ TCXO - Crystal Oscillator

## Slide 3
Clock Tree
TCXO
PLL
RCG
Branch
HW
TCXO = 19.2 MHz to 76.8 Mhz
Video, Camera, Graphics, --> 500MHz - 2000MHz

## Slide 4
PLL
PLL --> Phase lock loop --> Frequency multiplier
Fout = 19.2 * (L + M/N)
L, M, N are PLL registers for freq selection
Fout = 19.2 * (L + alpha)
192MHz ---> L=10 , alpha = 0
Consumer ask for 200MHz -->
L --> 10 + alpha----> 1 = 11 freq= 19.2*11 = 211.2
clk_set_rate(211.2MHz)
--------------------------------------------------------------
L --> 10 + alpha----> 0 = 10 freq= 19.2*10 = 192
clk_set_rate(211.2MHz)

## Slide 5
PLL
PLL has four outputs ---> main, odd, even, test
CXO --> PLL --> Pll main
CXO --> PLL --> Pll Odd
CXO --> PLL --> Pll Even
CXO --> PLL --> Pll Test
CXO --> 19.2
PLL0_main --> 600
pll0_odd --> 200
pll0_even --> 300
PLL
PLL Main
PLL Odd
PLL Even
PLL Test
CXO

## Slide 6
RCG
HW
150 MHZ
PLL Main
PLL Odd
PLL Even
PLL Test
CXO
600
200
300
RCG

## Slide 7
RCG
RCG --> Multiplexer --> Multiple inputs/single output --> output freq depends on the input we choose
RCG --> inbuilt divider Fout = Fin/divider; --> 150MHz
CFG_RCGR = Clock Generator Configuration Register
CFG_RCGR:: The SRC_DIV bits define the integer and half integer portion of the divider setting.
SRC_DIV = 2n-1 = 2(1.5)-1 = (3-1)= 2
SRC_DIV = 2
CFG_RCGR, CMD_RCGR

## Slide 8
RCG
For example for RCG:
for 5MHz output:
F(P_GCC_GPLL0_OUT_EVEN, 1, 1, 2);
if P_GCC_GPLL0_OUT_EVEN = 300Mhz
fout= (fin/d)*(m/n)
= (300/1)*(1/2)
= 300 * (1/2)
=150 Mhz
m/n regester can be replace by Alpha regester.

## Slide 9
Branch
CBC --> And Gate --> It can block the i/p clock if CBC is off, if it is ON, it allows the clock
CBCR --> bit 0 is to enable/disbale the clock, bit 31 is status.
PLL Main
PLL Odd
PLL Even
PLL Test
CXO
600
200
300
RCG
CBC
HW

## Slide 10
Thanks